## Slide 1
Data Encryption and Transmission Based on ESP32 Boards
Group members:
Jialun KOU
Han BAO
Andi SULA

## Slide 2
Introduction
This project aims to design a data exchange platform that meet data availability, integrity, and authentication. In general , the project will be split into three steps:
Step One: Ensuring the availability of data. make data accessible in real-time to any user visiting the broker server (Public mode)
Step three: Ensuring data integrity and authentication by implementing a security protocol.
If the user have no permission , then the user cannot access data from broker.
(Security mode)
Step two: able to switch public mode to security mode by pushing button

## Slide 3
Schematic
DH 11 Sensor
ESP-32
Button
We will use DHT11 sensor to collect temperature and humidity data from the room, then the temperature and humidity data will be processed and transmitted by ESP32.
Red led indicate the connection status of wifi and mqtt broker
White led indicate the status of mode

## Slide 4
What is ESP32?
The ESP32 is a microcontroller that is designed for low-power, connected applications.
How ESP32 communicate with MQTT broker ?
It has built-in Wi-Fi functionality, which allows it to connect to wireless networks and communicate with MQTT broker.

## Slide 5
MQTT broker
ESP32-A
ESP32-B
ESP32-A: Humidity & Temperature
Topic A: ESP32-A: Humidity & Temperature
Topic B: ESP32-B: Humidity & Temperature
ESP32-B: Humidity & Temperature
ESP32-B: Humidity & Temperature
ESP32-A: Humidity & Temperature
Node-Red as a user access and plot temperature and humidity chart in real time
Public mode
We will use an MQTT broker as server to exchange data between ESP32 devices.

## Slide 6
Node red Result (public mode )

## Slide 7
Core
WIFI
Connection check
Core1
Core0
From Single Core to Dual Core
DATA Process
&
transmission
MQTT
Connection check
MQTT
Connection check
WIFI
Connection check
By using a dual-core design can solve this problem , the ESP32 can dedicate one core to handle the Wi-Fi and MQTT connection , while the other core can be used to process sensor data. This allows the ESP32 to handle network connectivity and data processing concurrently, without compromising performance.
However, For the single core case . running the Wi-Fi stacks can consume a significant amount of processing power, which can impact the performance of other tasks running on the microcontroller.
DATA Process
&
transmission
To ensure the availability of data, the ESP32 devices need periodically check wifi and mqtt connection status and fix any disconnections on their own.

## Slide 8
Compare the performance between Single Core and Dual Core

## Slide 9
Order and Priority issue
Core1
Core0
MQTT
Connection check
WIFI
Connection check
Since the MQTT connection is dependent on the WiFi connection, To ensure secure and efficient data transmission, the ESP32 devices establish the WiFi connection first, before attempting to establish the MQTT connection.
Data processing and transmission tasks are only initiated once both connections are securely established
To maintain data availability, the ESP32 devices regularly check the status of both connections and fix any disconnections. The priority for connection checking is given to WiFi over MQTT."
To ensure this, we can use semaphores and multitask scheduling.
DATA Process & transmission

## Slide 10
Multi-task scheduling for core 1
Button switch mode
Sensor-sem give

## Slide 11
MQTT
borker
ESP32-A
ESP32-B
ESP32-A Encrypted Data
Topic A: ESP32-A Encrypted Data
Topic B: ESP32-B Encrypted Data
ESP32-B Encrypted Data
ESP32-B Encrypted Data
ESP32-A Encrypted Data
Security mode
Ensuring data integrity and authentication by implementing a security protocol. (Security mode)
In this case , if the user have no permission , then user cannot access data from broker

## Slide 12
Temperature
2 bytes
Humidity
2 bytes
Sensor
Temperature
2 bytes
Humidity
2 bytes
Plain Text
4 bytes
Temperature
2 bytes
Humidity
2 bytes
Padded Plain Text
16 bytes
Pkcs5 Padding
0C 0C 0C 0C 0C 0C 0C 0C 0C 0C 0C 0C
0C × 12
Security mode

## Slide 13
Padded Plain Text
16 bytes
16 bytes AES Key
AES Cipher
16 bytes
AES Cipher
16 bytes
HMAC
Key
Hash
Algorithm
Authentication Data
32 bytes
Integrity Data
32 bytes
AES Cipher
16 bytes
Authentication Data
32 bytes
Integrity Data
32 bytes
Length of AES Cipher
1 byte
Final Ciphered Data
Data encryption

## Slide 14
MQTT
broker
ESP32-A
ESP32-B
ESP32-A Encrypted Data
Topic A: ESP32-A Encrypted Data
Topic B: ESP32-B Encrypted Data
ESP32-B Encrypted Data
ESP32-B Encrypted Data
ESP32-A Encrypted Data
Security mode
Encrypted data seen from MQTT

## Slide 15
AES Cipher
16 bytes
Authentication Data
32 bytes
Integrity Data
32 bytes
Length of AES Cipher
1 byte
(Assume 16 here)
Divide According to the Last byte
i.e first 16 bytes
AES Cipher
16 bytes
Authentication Data
32 bytes
From
16 to
16 + 31
From
16 + 32 to
16 + 63
Integrity Data
32 bytes
Authentication Check
Integrity Check
PASS
PASS
16 bytes
AES key
Temperature
2 bytes
Humidity
2 bytes
Plain Text
4 bytes
AES Cipher
16 bytes
Unpadding
Data decryption

## Slide 16
Result
Data encryption

## Slide 17
Thank you for listening