## Slide 1
Data Encryption and Transmission Based on ESP32 Boards
Group members:
Jialun KOU
Han BAO
Andi SULA

## Slide 2
Core
WIFI
Core1
Core0
MQTT
Sensor
Sensor
MQTT
WIFI
From Single Core to Dual Core

## Slide 3
Core 0
Core 1
Serial Monitor
Queue
。。。。。。。
Queue of Dual Core

## Slide 4
Compare between Single Core and Dual Core

## Slide 5
Multi-task scheduling

## Slide 6
Temperature
2 bytes
Humidity
2 bytes
Sensor
Temperature
2 bytes
Humidity
2 bytes
Plain Text
4 bytes
Temperature
2 bytes
Humidity
2 bytes
Padded Plain Text
16 bytes
Padding
0C 0C 0C 0C 0C 0C 0C 0C 0C 0C 0C 0C
0C × 12
Data encryption

## Slide 7
Padded Plain Text
16 bytes
16 bytes AES Key
AES Cipher
16 bytes
AES Cipher
16 bytes
HMAC
Key
Hash
Algorithm
Authentication Data
32 bytes
Integrity Data
32 bytes
AES Cipher
16 bytes
Authentication Data
32 bytes
Integrity Data
32 bytes
Length of AES Cipher
1 byte
Final Ciphered Data
Data encryption

## Slide 8
AES Cipher
16 bytes
Authentication Data
32 bytes
Integrity Data
32 bytes
Length of AES Cipher
1 byte
(Assume 16 here)
Divide According to the Last byte
i.e first 16 bytes
AES Cipher
16 bytes
Authentication Data
32 bytes
From
16 to
16 + 31
From
16 + 32 to
16 + 63
Integrity Data
32 bytes
Authentication Check
Integrity Check
PASS
PASS
16 bytes
AES key
Temperature
2 bytes
Humidity
2 bytes
Plain Text
4 bytes
AES Cipher
16 bytes
Unpadding
Data decryption

## Slide 9
Server
ESP32-A
ESP32-B
ESP32-A: Humidity & Temperature
Topic A: ESP32-A: Humidity & Temperature
Topic B: ESP32-B: Humidity & Temperature
ESP32-B: Humidity & Temperature
ESP32-B: Humidity & Temperature
ESP32-A: Humidity & Temperature
Send to Node-Red and plot
Data transmission and receiving

## Slide 10
Server
ESP32-A
ESP32-B
ESP32-A Encrypted Data
Topic A: ESP32-A Encrypted Data
Topic B: ESP32-B Encrypted Data
ESP32-B Encrypted Data
ESP32-B Encrypted Data
ESP32-A Encrypted Data
Encrypted data transmission and receiving

## Slide 11
Result
Un-encrypted data seen from MQTT
Encrypted data seen from MQTT
Data encryption

## Slide 12
Result

## Slide 13
Thank you for listening